## Slide 1
THUMB INSTRUCTION REFERENCE
13 Instructions from Real Disassembly
Every distinct Thumb mnemonic in rec_sum / main / Reset_Handler — simplest to most complex
arm-none-eabi-objdump -S · main.o & firmware.elf

## Slide 2
LEVEL 1 · DATA MOVEMENT · 1 OF 13
MOV / MOVS
Copy a value into a register — from an immediate or another register
FROM THE LISTING
30: movs r3, #0
34: movs r0, #10
1c: mov r2, r0
movs loads an 8-bit immediate and updates the N/Z flags. Plain mov (the “high-register move” encoding) copies register-to-register without touching flags — used here right after a compare, so the flags survive.
WHAT IT DOES
The simplest data-processing instruction — no arithmetic, just a copy.
MOVS Rd, #imm8: 16-bit encoding, low registers only, sets flags (S = “sets flags”).
MOV Rd, Rm (hi-register form): works on any register r0–r15, including sp/pc, and never sets flags — this is why the compiler picks it for “quiet” copies like mov sp, r7.

## Slide 3
LEVEL 1 · DATA MOVEMENT · 2 OF 13
ADD / ADDS
Add two values; used for arithmetic and for stack-frame bookkeeping
FROM THE LISTING
4: add r7, sp, #0
20: add r3, r2
24: adds r7, #8
add r7, sp, #0 sets up the frame pointer (SP-relative add, no flags). adds r7, #8 tears the frame back down and does set flags. add r3, r2 is plain arithmetic (a + b) using the hi-register form.
WHAT IT DOES
Same register/immediate pattern as MOV: the S suffix (ADDS) sets flags, plain ADD (register-to-register hi form or SP-relative) does not.
Used both for real arithmetic (int c = a + b) and for silently adjusting r7/sp when setting up or tearing down a stack frame.

## Slide 4
LEVEL 1 · DATA MOVEMENT · 3 OF 13
SUB / SUBS
Subtract; also used to reserve space on the stack
FROM THE LISTING
2: sub sp, #8
14: subs r3, #1
sub sp, #8 is a special SP-immediate encoding that reserves 8 bytes of stack for local variables — pure bookkeeping, no flags. subs r3, #1 computes i-1 for the recursive call and does set flags.
WHAT IT DOES
sub sp, #imm is how a function prologue allocates its local-variable stack frame — conceptually just “move the stack pointer down”.
subs Rd, #imm8 is the arithmetic form the source code actually asked for (i - 1), and sets N/Z/C/V like any flag-setting instruction.

## Slide 5
LEVEL 1 · DATA MOVEMENT · 4 OF 13
CMP
Compare two values by subtracting them, keeping only the flags
FROM THE LISTING
8: ldr r3, [r7, #4]
a: cmp r3, #1
c: dc01 bgt.n 12
Implements if(i <= 1): loads i into r3, compares it with 1. CMP never stores a result — it exists purely to set flags for the branch that follows.
WHAT IT DOES
Internally the same subtraction hardware as SUB, but the result is discarded — only N, Z, C, V are updated.
Always paired with a conditional instruction afterward (here, a conditional branch) — CMP alone changes nothing observable.

## Slide 6
LEVEL 2 · MEMORY ACCESS · 5 OF 13
STR
Store a register's value into memory, base register + immediate offset
FROM THE LISTING
6: str r0, [r7, #4]
32: str r3, [r7, #4]
Both spill a value from a register into its stack slot — the first stores the incoming parameter i, the second stores the local variable sum, each 4 bytes above the frame pointer r7.
WHAT IT DOES
Addressing mode: [base register, #offset] — the address is base + offset, computed once, not modified.
This is how C local variables that don't fit in registers (or that have their address taken) end up living on the stack.

## Slide 7
LEVEL 2 · MEMORY ACCESS · 6 OF 13
LDR
Load a register's value back from memory, same addressing mode as STR
FROM THE LISTING
8: ldr r3, [r7, #4]
1e: ldr r3, [r7, #4]
The mirror image of STR: reads the value back out of its stack slot into a register so it can be used in a computation (the comparison, and later the final addition).
WHAT IT DOES
Same [base, #offset] addressing as STR — LDR and STR are a matched pair, one direction each way.
A local variable in C is typically stored once and loaded every time it's read — this pattern repeats throughout both functions.

## Slide 8
LEVEL 2 · MEMORY ACCESS · 7 OF 13
LDR (literal)
Load a constant that's too large to fit in an immediate, from a literal pool near the code
FROM THE LISTING
8000064: ldr r0, [pc, #40]
@ (8000090 <...>)
8000090: .word 0x080000a6
Reset_Handler needs full 32-bit addresses (_sidata, _sdata, etc.) that can't be encoded as an immediate operand. The assembler stores them as data words right after the code and loads them PC-relative.
WHAT IT DOES
Uses PC as the base register instead of a general-purpose register — the offset points forward into the instruction stream, at data the assembler placed there (the “literal pool”).
This is the standard Thumb trick for materializing large constants and addresses, since instructions can't embed a full 32-bit immediate.

## Slide 9
LEVEL 2 · MEMORY ACCESS · 8 OF 13
LDR.W / STR.W
Wide (32-bit) load/store with post-indexed addressing — auto-increments the base register
FROM THE LISTING
800006e: ldr.w r3, [r0], #4
8000072: str.w r3, [r1], #4
The FLASH→RAM copy loop in Reset_Handler: load a word from r0, then bump r0 by 4; store a word to r1, then bump r1 by 4 — all in one instruction each.
WHAT IT DOES
“Post-indexed”: the transfer uses the base register's current value, then the base register is updated afterward — no separate add instruction needed.
The .W suffix forces the 32-bit Thumb2 encoding, which is what makes post-indexing (and the full r0–r15 register range) available — Thumb1's narrow LDR/STR can't do this.

## Slide 10
LEVEL 3 · CONTROL FLOW · 9 OF 13
B / B.n
Unconditional branch — jump to a PC-relative target, always taken
FROM THE LISTING
e: ldr r3, [r7, #4]
10: b.n 22 <rec_sum+0x22>
Implements the return i; path of the if/else: after loading i, jump straight past the recursive-call code to the function epilogue at offset 0x22.
WHAT IT DOES
“.n” marks the narrow 16-bit encoding — short-range branches (a few hundred bytes) fit in 16 bits; longer ones would need B.W.
Also used as the loop-back branch in copy_data_loop / zero_bss_loop, and as the infinite b . trap after bl main.

## Slide 11
LEVEL 3 · CONTROL FLOW · 10 OF 13
BGT / BGE
Conditional branch — only taken if the flags from a prior CMP satisfy the condition
FROM THE LISTING
a: cmp r3, #1
c: bgt.n 12 <rec_sum+0x12>
8000080: bge.n 8000088
bgt.n implements if(i <= 1): branch taken only when i > 1 (i.e. skip the base case). bge.n implements the loop-exit test cmp r1,r2 / bge done in both copy loops.
WHAT IT DOES
Same 16-bit branch encoding as B, but gated by a condition code (GT = signed greater-than, GE = signed greater-or-equal) evaluated from N/Z/C/V.
This is how Thumb2 compiles every if/while/for condition when the body is too large to fit in an IT block — compare, then branch around.

## Slide 12
LEVEL 3 · CONTROL FLOW · 11 OF 13
PUSH / POP
Transfer a list of registers to/from the stack in a single instruction
FROM THE LISTING
0: push {r7, lr}
28: pop {r7, pc}
8000040: push {r7}
800005e: pop {r7}
rec_sum saves r7 and lr on entry (it calls itself, clobbering lr) and restores both on exit — popping straight into pc performs the return. main() in firmware.elf never calls another function, so it only pushes/pops r7, leaving lr untouched.
WHAT IT DOES
One instruction moves an entire register list — far more compact than one push/pop per register.
pop {…, pc} is a common return idiom: it restores registers and returns in the same instruction, no separate branch needed.
Whether lr appears in the list depends entirely on whether the function calls anything else (compare rec_sum vs. this main).

## Slide 13
LEVEL 4 · SUBROUTINE LINKAGE · 12 OF 13
BL
Branch with Link — call a function, saving the return address into LR
FROM THE LISTING
18: bl 0 <rec_sum>
36: bl 0 <rec_sum>
8000088: bl 8000040 <main>
rec_sum calls itself recursively; main calls rec_sum(10); Reset_Handler calls main — three different call sites, same instruction. Each one overwrites LR with the address right after the BL.
WHAT IT DOES
The only “call” instruction in Thumb — always a 32-bit encoding, since it needs enough bits for a large PC-relative call offset.
Because BL overwrites LR, any function that itself calls another function (like rec_sum, calling itself) must PUSH/POP {lr} to avoid losing its own return address.

## Slide 14
LEVEL 4 · SUBROUTINE LINKAGE · 13 OF 13
BX
Branch and Exchange — jump to an address held in a register
FROM THE LISTING
8000060: bx lr
firmware.elf's main() is a leaf function — it never calls anything else, so LR still holds its original caller's return address untouched. It restores r7, then returns directly via bx lr instead of popping pc.
WHAT IT DOES
“Exchange” refers to switching between ARM and Thumb instruction sets based on bit 0 of the target address — on Cortex-M3 (Thumb-only) that just means “branch there”.
The two ways to return — pop {…, pc} vs. bx lr — both appear in this listing, depending on whether the function pushed lr onto the stack in the first place.

## Slide 15
SUMMARY
Four Levels, Thirteen Instructions
Level 1 — Data Movement
MOV/MOVS · ADD/ADDS · SUB/SUBS · CMP
Level 2 — Memory Access
STR · LDR · LDR (literal) · LDR.W/STR.W
Level 3 — Control Flow
B/B.n · BGT/BGE (Bcond) · PUSH/POP
Level 4 — Subroutine Linkage
BL · BX