## Slide 1
STARTUP FILE & LINKER SCRIPT
From Power-On to main()
A line-by-line walkthrough of startup_stm32f103.s and STM32F103C8.ld
STM32F103C8T6 · Cortex-M3 · Thumb2 · Bare-metal

## Slide 2
OVERVIEW
Two Files, One Job
Before a single line of your C code can run, something has to tell the CPU where the stack begins and what to execute first — and make sure global variables hold sane values. On bare metal, you provide both.
S
Startup File
startup_stm32f103.s
Defines the vector table — the hardware-mandated array of addresses at the base of FLASH
Implements Reset_Handler: the very first code to run after reset
Copies .data from FLASH to RAM and zero-fills .bss before main() is safe to call
L
Linker Script
STM32F103C8.ld
Declares where FLASH and RAM physically live on this exact chip
Places the vector table, code, and constants into FLASH
Splits variables into .data (needs a FLASH-stored initial value) and .bss (just needs zero), and exports the boundary symbols the startup file needs
They are tightly coupled: the startup file references symbols that only exist because the linker script defines them.

## Slide 3
HARDWARE LAYOUT
STM32F103C8T6 Memory Map
FLASH — Code Storage
0x08000000 – 0x0800FFFF (64 KB)
.isr_vector → .text → .rodata → initial values for .data
RAM — Working Memory
0x20005000 (top) = _estack
Initial stack pointer — stack grows downward ↓
… stack space …
.bss
Zero-initialized globals
.data
Initialized globals (writable RAM copies)
0x20000000 (bottom, 20 KB total)
0x08000000 and 0x20000000 are fixed by ARM's Cortex-M memory map convention and ST's sizing for the “C8” density variant (64 KB FLASH / 20 KB RAM).

## Slide 4
LINKER SCRIPT · PART 1
ENTRY and the MEMORY Block
ENTRY(Reset_Handler)
MEMORY
{
FLASH (rx) : ORIGIN = 0x08000000, LENGTH = 64K
RAM (rwx) : ORIGIN = 0x20000000, LENGTH = 20K
}
ENTRY doesn't control boot electrically — Cortex-M3 always boots via the vector table. It sets the ELF header's entry field for debuggers and tools like objdump/gdb.
ORIGIN / LENGTH come straight from the chip's datasheet for each named region.
(rx) on FLASH — readable + executable, not writable. Flash can't be written like a variable; it needs a special programming sequence.
(rwx) on RAM — readable, writable, executable. Variables that change at runtime must live in writable memory.

## Slide 5
LINKER SCRIPT · PART 1
_estack and .isr_vector Placement
_estack = ORIGIN(RAM) + LENGTH(RAM);
0x20000000 + 0x5000 = 0x20005000 — one past the last valid RAM byte.
ARM stacks grow downward, so “empty” SP starts at the top of RAM.
Consumed by the startup file as word 0 of the vector table — the value the CPU loads into SP at power-on.
.isr_vector :
{
KEEP(*(.isr_vector))
} > FLASH
Placed at 0x08000000 — not convention, a hardware requirement. Cortex-M3 reads word 0 (SP) and word 1 (reset vector) from this exact address on reset.
KEEP() matters because nothing in C “calls” this table by name — without it, --gc-sections would discard it as unused.

## Slide 6
LINKER SCRIPT · PART 1
.text and .data — the FLASH/RAM Trick
.text :
{
*(.text*)
*(.rodata*)
} > FLASH
_sidata = LOADADDR(.data);
.data :
{
_sdata = .; *(.data*) _edata = .;
} > RAM AT> FLASH
Initialized globals need to be writable (RAM) but must start with a real value (stored in FLASH). “> RAM AT> FLASH” gives the section a runtime address in RAM and a load address in FLASH — both at once.
_sidata
Initial values' location in FLASH (copy source)
_sdata
Start of .data in RAM (copy destination start)
_edata
End of .data in RAM (copy destination end)
These symbols do nothing by themselves — Reset_Handler must explicitly copy FLASH → RAM using them.

## Slide 7
LINKER SCRIPT · PART 1
.bss — Zero-Initialized Globals
.bss :
{
_sbss = .;
*(.bss*)
*(COMMON)
_ebss = .;
} > RAM
Handles globals with no initializer (int total;) — C guarantees these start at zero.
No reason to waste FLASH storing zeros — the linker just reserves RAM space and records _sbss / _ebss.
*(COMMON) catches old-style “tentative definitions” some toolchains group separately from ordinary .bss.
Nothing hardware-level zeroes this region — like .data, Reset_Handler must do it explicitly before main() runs.

## Slide 8
STARTUP FILE · PART 2
The Vector Table
g_pfnVectors:
.word _estack /* SP */
.word Reset_Handler /* Reset */
.word Default_Handler /* NMI */
.word Default_Handler /* HardFault */
...
1
Word 0 — Initial SP
The Cortex-M3 reset sequence, done entirely in hardware, loads this value directly into the SP register — before any code has run.
2
Word 1 — Reset Vector
The address the core jumps to next: Reset_Handler. Bit 0 is set to mark it as Thumb code, handled automatically by the assembler/linker.
The remaining entries are core exceptions and, in a real project, the full peripheral IRQ list — here they all point at Default_Handler as placeholders.

## Slide 9
STARTUP FILE · PART 2 · STEP 1
Reset_Handler — Copy .data to RAM
ldr r0, =_sidata
ldr r1, =_sdata
ldr r2, =_edata
copy_data_loop:
cmp r1, r2
bge copy_data_done
ldr r3, [r0], #4
str r3, [r1], #4
b copy_data_loop
copy_data_done:
r0 walks FLASH from _sidata (stored initial values); r1 walks RAM from _sdata (where live variables belong).
One 32-bit word copied per loop iteration: ldr post-increments r0, str post-increments r1.
Loop continues until r1 reaches _edata.
After this, every initialized global variable holds the value your C source specified.

## Slide 10
STARTUP FILE · PART 2 · STEPS 2–3
Zero .bss, Then Call main()
ldr r1, =_sbss
ldr r2, =_ebss
movs r3, #0
zero_bss_loop:
cmp r1, r2
bge zero_bss_done
str r3, [r1], #4
b zero_bss_loop
zero_bss_done:
bl main
b .
Same copy pattern, simpler: no source data, just write constant 0 across _sbss–_ebss.
Guarantees every uninitialized global starts at zero, as C requires — RAM otherwise holds unpredictable leftover contents.
Only now is it safe to enter C
Stack is set by hardware, .data is copied, .bss is zeroed — every global holds a value C code is entitled to assume it has. bl main hands off control; the trailing b . traps the core if main() ever returns, which it isn't meant to on a freestanding target.

## Slide 11
SYNTHESIS
How the Two Files Connect
Symbol | Defined In | Used In | Purpose
_estack | Linker script | Startup file (vector table word 0) | Initial stack pointer
Reset_Handler | Startup file | Linker (ENTRY) & startup (vector table word 1) | First code after reset
_sidata / _sdata / _edata | Linker script | Startup file (.data copy loop) | FLASH→RAM copy bounds
_sbss / _ebss | Linker script | Startup file (.bss zero loop) | Zero-fill bounds
.isr_vector placement | Linker script | Hardware (reads 0x08000000 directly) | Boot-time SP & reset address
Neither file compiles into anything meaningful alone: the startup file's symbol references are undefined without the linker script, and the linker script's layout is pointless without Reset_Handler to act on it.

## Slide 12
KEY TAKEAWAY
Everything C Assumes, Someone Has to Set Up First
Hardware sets the stack pointer from word 0 of the vector table — before any instruction runs.
Reset_Handler copies .data from FLASH to RAM and zero-fills .bss — before main() is entered.
Only after both steps does every global variable hold the value C code is entitled to assume it has.
This example truncates the IRQ table to core exceptions only and skips clock configuration (SystemInit / HSE / PLL) — a production project extends both.